## Slide 1
SAR Basics and Radar Signal Interaction with Snow and Ice
Helmut Rott
ENVEO IT, Innsbruck
& University of Innsbruck, Austria
ESA LTC, 16-20 September 2024, Innsbruck

## Slide 2
Basic components and concepts of imaging radar systems
SAR image formation
SAR signal characteristics
Satellite SAR operation modes
SAR geometry and image features in complex terrain
Characteristics of complex radar backscatter signals
Dielectric and scattering properties of snow and ice
Basics of across-track SAR interferometry
InSAR procedures and examples for mapping surface topography and ice motion
Contents of the Lecture

## Slide 3
Radar Frequency Bands and Atmospheric Transmittance
One-way atmospheric transmittance for Standard Atmosphere
---- with stratus (z = 500 m) ; - · - · stratocumulus, (z = 2 km)
 Absorption bands

## Slide 4
Basic Equation for Radar Scattering Measurement
σ° – Radar cross section per unit area (distributed target)
G = 4Aa/2 - Antenna Gain (Aa – Antenna area)
Radar Equation
Bistatic
Monostatic
Bistatic Radar Configuration
P Power [W]
G Antenna Gain
R Range
 Scattering Cross Section
i Radar cross section of incremental scattering element
A i Size of scattering element
A 0 Surface resolution cell

## Slide 5
Basic Components of SAR Systems
R0
Total time delay: 2 R0/c
In order to digitize the complex input radar signal, it is split in two components, in which the phase of one component is shifted by 90°:
The in-phase (I) and quadrature (Q) components.
I = A cos  ; Q = A sin 
A2 = I2 + Q2 ;  = arctan (Q/I)
A - Amplitude

## Slide 6
Geometry and Resolution of Imaging Radar Sensors
t
R
Slant range resolution
ra = R/L Real aperture
 Real aperture
beamwidth a = /L [rad]
Dense azimuth sampling required:
PRF > 2v/L (signal Doppler BW)
Synthetic aperture
Virtual beamwidth
SA = /LSA
Spatial Resolution
ra = L/2 Azimuth resolution
Synthetic aperture
rr = c/2 Slant range resol.
rg = rr/sin θi Ground range res.

## Slide 7
SAR Image Formation – Range Compression
Half power (3dB)
beamwidth:
Slant range
r = 0.866 /Da [rad]
Azimuth
a = 0.866 /La
Footprint (azimuth)
Wa = ( R) /La
The uncompressed pulse length is several sec
Linear frequency modulation (chirp) for improving range resolution:
The frequency changes during one pulse from 0 to (0 +)
Chirp (Range) Bandwidth: BR = (0 +) - 0  =   
The pulse is de-compressed using a replica of the transmitted chirp
Compressed pulse length: c  1/BR  range resolution rr = c/2
Fig. R. Hanssen, 2001
Transmitted waveform De-chirped waveform
Slant range compression
Chirp
BR = 100 MHz  rr = 1.50 m

## Slide 8
SAR Image Formation – Range / Doppler Algorithm
Fig. Moreira et al. 2013
Geometry for Doppler shift estimate
Main SAR processing steps: Range and azimuth compression by convolution with the corresponding reference functions.
Doppler frequency shift: ;
t
0 and t0 refer to across track direction (zero Doppler)
 squint angle

## Slide 9
SAR Image Formation – Example for Point Target
Along-track point target signal
time 
phase
amplitude
chirp (faz)
X-SAR Amplitude Image of Corner Reflector
CR edge length 1.8 m
Pixel spacing (range x azimuth) 6.66 m x 4.88 m
SIR-C/X-SAR test site Ötztal, Oct. 1994
Chirp BW 20 MHz, Range res. 7.5 m
Azimuth res. 7.1 m

## Slide 10
SAR Signal Characteristics
Signal scattered back from a medium that is composed of many small scattering elements within a SAR resolution cell:
The signal is the coherent sum of contributions from all (n) elemental scatterers (e) in the resolution cell Ae,nexp[ie,n], accounting also for the differential path delays re,n between the scatterers and the wave front.
Du to this effect the amplitude of distributed targets in a SAR image show a noisy pattern, called speckle.
Speckle is spatially random multiplicative noise due to coherent superposition of multiple backscatter sources within a SAR resolution cell.
If the scattering properties of a target are preserved the speckle pattern is conservative  images suitable for repeat-pass InSAR processing.
re,n
.

## Slide 11
Probability Density Functions for Exponentially and Rayleigh Distributed Variables
Ulaby & Long, 2014
 Mean value ;  Standard deviation
Statistical distribution of amplitude (A = P) of homogeneous distributed target: Rayleigh distribution
Statistical distribution of power (P) of homogeneous distributed target for N number of looks:
N = 1 Exponential PDF
N > 1 2 - PDF with 2N degrees of freedom
Standard dev. over N independent resolution cells: (N) =/N
PDF for phase of SAR signal: Uniformly distributed

## Slide 12
Probability Density Functions and Example for Despeckling
PDF for power (P) for N >1: Chi-square distribution,2 = (2P/P)
Standard deviation for N number of looks: P(N) = P/(N)
Single Look:
PDF for amplitude (A): Rayleigh distribution
Standard dev. for N number of looks: A(N) = 0.523 A/(N)
X-band SAR image 3 m resolution
N = 2
Despeckling with gamma Map filter (structure preserving low-pass filter)
11x11 window size
Oliver & Quegan, 1998

## Slide 13
SAR Satellite Missions for Earth Observation (Sample)
Sensor Satellite [GHz]. Resolution/Swath Repeat option
Past
AMI ERS-1,-2(1991-2011) 5.3 VV 25 m - 100 km 35d / 1 d
SIR-C/X-SAR Shuttle (1994) 1.2,5.3,9.6 25 m / 40 km 2 campaigns
SIR-C/X-SAR SRTM (Feb.2000) 5.3, 9.6 50/100 m / 100/200 InSAR DEM
ASAR Envisat (2002-12) 5.3 30,100,1000 -/ 100-400 km 35 d
Present
SAR Radarsat2 (2007-) 5.4 3, 10, 30 m, / 20 km 24 d
TerraSARX TerraSAR-X(2007-) 9.6 1, 3,10 m / 10,30,100 km 11 d
TerraSARX TanDEM-X (2010-) 9.6 in Tandem with TerraSAR-X 11 d, SP-InSAR
SAR2000 COSMO-SkyMed(2007- 9.6 3m .. 100 m / 10-100 km 1d..16d, 4 Sat.
CSAR Sentinel-1 (2013-) 5.4 5m ….40 m / 80 … 410 km 12 d
PALSAR-2 ALOS-2 (2014-) 1.27 3m….100 m / 25 …. 490 km 14 d
X-Band SAR ICEYE Constell. (2018-) 9.6 1m …. 15 m /5 …. 100 km daily, 17 Sat.
SAR-L SAOCOM (2018- ) 1.27 10m… 100 m / 20 … 350 km 16d, 8d 2 Sat
CSAR Radarsat Constell.(2019 -) 5.4 3 m …100m / 20 …500 km 12d, 4d, 3 Sat.
Future
L/S-SAR NISAR (2025-) 1.25, 3.2 3m ….48 m / …. 240 km 12 d
P-Band SAR BIOMASS (2025-) 0.435 50 m / 150 km 3d …228 d
L-Band SAR ROSE-L (2027-) 1.25 10m ….100m / …..260 km 12 d
Passive C-band HARMONY (2028-) 5.4 2-satellite constellation using S1 active signal
BIOMASS
NISAR

## Slide 14
Sentinel-1 SAR Operation Modes
ESA SP-1322/1
Main characteristics of the Sentinel-1 nominal measurement modes
Sub-swath | Bandwidth | Slant Range resolution
IW1 | 56.5 MHz | 2.65 m
IW2 | 48.3 MHz | 3.11 m
IW3 | 42.8 MHz | 3.50 m
Typical numbers for IW mode bandwidth

## Slide 15
TanDEM-X - Formation Flying Radar Mission
Data modes for DEM acquisition
Pursuit monostatic Bistatic Alternating bistatic
Krieger et al., 2013
Helix satellite formation for DEM acquisition
TanDEM-X (TerraSAR-X add-on for Digital Elevation Measurements) is a spaceborne radar interferometric mission that is based on two TerraSAR-X satellites flying in close formation. Primary objective is DEM acquisition.
Radar instrument characteristics

## Slide 16
Imaging Radar Geometry - Terrain Induced Distortions
Across track radar geometry
Image Plane
Surface resolution across track: r = c/(2sini)
i Local incidence angle
Tandem-X, 2021-11-13, VV HH, h = 30.5°
Slant range
Azimuth
Layover
Vent

## Slide 17
IS 2 Track 437
h = 23°
ASAR IS 6 Track 308
h = 41°.
Inntal
Ötztal
LOS
Terrain Induced Distortions – Impact of Look Angle
LOS
Inntal
Ötztal
 Sölden
 Sölden

## Slide 18
 Direction of Illumination
LOS
LOS
Terrain Induced Distortions – Crossing Orbits
Hintertux
Hintertux

## Slide 19
Microwave Permittivity for snow
with density S = 0.45 g/cm³
Dielectric Properties of Snow and Ice
One-way power penetration length in wet snow:
Permittivity:
Ice: є‘ = 3.15 є‘‘ < 0.001 f (, T)
Dry snow:
є‘ =1.0 + 1.6  + 1.86 3 ;  in g cm-3
Wet snow:
є‘ = є‘ (dry) +  є
є = 0.23 Vw / [1 - i(/ 0)]
Vw [liquid water, volume %]
0  9 GHz, relaxation frequency of wet snow
є‘‘  0.5 in C-band with Vw= 6 %

## Slide 20
Microwave Penetration in Dry Snow and Firn
dL based on experimental data 
High Alpine snow (Mätzler, 1987)
Antarctic dry snow zone (Rott et al., 1993)
Inversion of satellite MW radiometer data, Antarctica
 Percolation zone of glaciers and ice sheets (frozen state)
Radiative transfer (RT) approach for dL
ka , ks [m-1] absorption & scattering coefficient
MW emission & backscatter measurements
Dronning Maud Land, Antarctica
z
Vertical section of near-surface layers
Percolation zone, Ekström Ice Shelf

## Slide 21
Radar Backscatter Signal for Dry Snow over Ground
dS
S
°t
1st order RT model, single layer
°t = °as + °v + 2as(°g2s)
 transmissivity air/snow interface
°as backscatter coeff. air/snow interface
°v snow volume backscatter. coeff.
°g backscatter coefficient of ground
s = exp(-keds/cos θ’) transmissivity
Backscatter contributions in dependence of radar frequency (single-layer DMRT model) i = 40°, effective grain size RE = 1.0 mm
 13.95 GHz 0 as function of snow depth with different grain size (Xu et al., 2010)
Volume scattering: the size of scattering elements is critical 

## Slide 22
Backscatter Signals of Dry and Wet Snow
Average backscatter coefficients for dry and wet snow over ground (meadow) by ground-based scatterometry
Test site: Leutasch
i
 Snow-free (meadow)
Dry snow (fine grained), low-loss medium, signal dominated by backscatter at subnivean ground
 Wet snow (high absorption losses)

## Slide 23
SAR Interferometry for Land Snow and Ice Applications
Configurations for Land Snow and Ice Observations
InSAR Configuration | Measurement Parameter | Applications
Across-track |  Look angle | DEM & topographic change
Across-track differential | r/t LOS displacement | Ice motion, surface deformation
Differential | /t phase delay | Change in snow mass, SWE
Across-track, multi-baseline tomography | backscatter intensity (azim., range, z) | Internal structure of glaciers and ice sheets
Coherently Received Signal of a Point Scatterer
Interferogram computation: V (m,n) = V1 (•) V2* (•) = |V1 (•)| |V2 (•)| exp [i  (•)]
SAR echo image Nr. 1: V1(m,n) = | V1 (m,n) | exp [i 1(m,n)]
SAR echo image Nr. 2: V2 (m,n) = | V2 (m,n) | exp [i 2(m,n)]
amplitude phase
Interferometric phase:  (m,n) =  1 (m,n) -  2 (m,n)
m,n – range, azimuth coordinate of pixel
V* complex conjugate
Absolute phase of received signal:
phase of surface scattering element

## Slide 24
Interferometric Coherence of Snow and Ice
Total normalized coherence:
Related to processing parameters, minor loss in coherence by choosing suitable configurations
SNR Related to thermal noise, critical for wet snow due to low σ°
Volume Volumetric decorrelation, due to penetration in dry snow and firn; depends on baseline and snow microstructure
Temp Temporal decorrelation; main factors for snow: surface melt, snowfall, snow drift (wind erosion and deposition) – impact depending on radar frequency
Complex correlation coefficient (coherence) of two SAR images
Wet snow
& ice
tot 3-day repeat pass C-band SAR data (ERS), Antarctic dry snow zone (Dronning Maud Land), no snowfall 
Dominated by Volume
ERS-1/2 One-day interferogram
Summer
Hintereisferner

## Slide 25
Coherence Estimate
Phase noise in dependence of coherence and number of resolution elements (number of looks, NL)
NL = 1
NL = 4
For accurate coherence estimates window (W) size with large NL is needed
Estimate of 

Figs. R. Bamler

## Slide 26
Geometry of Across-Track SAR Interferometry
Phase Image 1:
Image 2:
Requirement for full coherence:  sce,1 =  sce,2
Relation between phase and difference in distance:
where
Interferogram: the phase  1,2 is given modulo 2
Wrapped Phase: -   
Bn – perpendicular
baseline
Graphic representation
)
)

## Slide 27
Across-Track InSAR –Topographic Mapping
Change across swath
 = ( 4/) R
For a non-moving target the total phase is made up by:
= (flat) + (topo)+ (atmos)
Iso-range line:
R = const.,  = const.
 = 2
(atmos): change in atmospheric phase delay

## Slide 28
Example for Interferograms with Flat Earth and Topographic Fringes
Interferograms (wrapped phase) in radar geometry
 Flat Earth and Topography
Topography 
Elevation contour lines
Simulated interferogram for a cone using ERS SAR parameters
i = 23°, Bn = 100m
2π
0
Interferogram geometrically corrected 
Unwrapped phase
2

## Slide 29
InSAR Sensitivity to Elevation and Impact of Penetration
Phase sensitivity to elevation
monostatic mode
Ha, Height of ambiguity
(height for  = 2)
Ha, orbit height 780 km,  = 23°
The InSAR-based elevation refers to the scattering phase centre, in dry snow and ice located below the surface.
The depth of the phase centre, Z, below the surface can be derived from the volumetric coherence Vol:
Height of ambiguity in volume:
Z derived from Vol (TanDEM-X) vs h (TDMX – optical DEM) at sites with different accumulation rates an snow/firn morphology, Union Glacier, Antarctica
Rott et al., 2021
Z
h

## Slide 30
InSAR DEM Differencing - Estimating Glacier Volume Change & Mass Balance
Surface elevation change (h/t) of Antarctic Peninsula Glaciers (Larsen B)
TDM CoSSC data acquired from same satellite track in winter (frozen snow/ice), with same °, coherence and  (repeat tracks)
Comparison of TDM with airborne lidar (ATM) data of NASA IceBridge - high agreement
h/t ATM - TDM
Mean difference 0.01 m/yr RMSD = 0.22 m/yr
2011-2013
-6.29 Gt/yr
2013-2016
-2.90 Gt/yr
Rott et al., 2018

## Slide 31
InSAR Glacier Motion - Interferogram
11 day repeat pass
1 Fringe = 1.5 mm/day LOS
TerraSAR-X interferogram (topography & motion) 2008/10/13 - 2008/10/24, Bn = 129 m
Topographic fringes
Shear zone -> decorrelation
Calving Front
Vc =0.25m/d
Sea Ice
0 km 2

## Slide 32
Across-track InSAR Measurement of Surface Displacement
RP- InSAR measures displacement in LOS of the radar beam
refers to the scattering phase centre
LOS
Across-track view
R
LOS: dis = (4/)R = (4/)(y sin  - z cos )
Band | X | C | L
R (2) = /2 | 1.56 cm | 2.83 cm | 12.50 cm
y
=

S/t = w + b local surface displacement
w - vertical shift of ice body
b - surface balance (melt)
vy

## Slide 33
3D Ice Motion and Surface Parallel Flow Assumption
InSAR from a single track yields one component of the velocity vector.
Observations from three directions are needed to obtain the 3D vector:
Vh horizontal velocity vector
True 3D vectors are obtained by InSAR if at least 3 sufficiently different LOS views are available.
By offset tracking using data from crossing orbits
Surface-parallel flow assumption – Approximation for 3D motion.
Assumes glacier surface in equilibrium state
Single track InSAR, Surface-parallel flow: LOS displacement projected onto surface in slope direction 
InSAR motion of crossing orbits: combines interferograms of ascending & descending orbits: provides magnitude and argument of 2D v in LOS/azimuth coordinates.
2D v is projected onto surface to obtain 3D velocity approximation

## Slide 34
Ice Motion based on Horizontal Flow Assumption
Magnusson et al., 2007
Topographically corrected interferogram
 Horizontal velocity field, assuming surface parallel flow; argument of vh derived from stacks of ascending and descending InSAR tracks
Radar LOS 
ERS1/2
27/28 03 1996
Skeidararjökull
Flow path of jökulhlaup

## Slide 35
Example for 3D Ice Motion based on Offset Tracking of Crossing Orbits
Chart: distance (m)
Horizontal flow velocity along centre line
Vertical displacement rates along centre line
Uplift & acceleration in late August related to rainfall
Chart: elevation change (m / d)
Doyle et al., 2015
TanDEM-X repeat pass image pairs of ascending & descending orbits:
4 projections of the displacement vector:
LOS & Along-track (Asc, Desc)
 3D Displacement

## Slide 36
 InSAR surface velocity from S1 6-day repeat images of winter campaigns, crossing orbits
InSAR applies data stacking; 50 m grid size
Requires non-melting surfaces
InSAR gaps in areas with high flow velocities near calving fronts (are filled by offset-tracking)
OT
InSAR
 Comparison of InSAR and Offset-tracking profiles across the ice divide (250 m grid)
Low velocities
Data available at:
http://cryoportal.enveo.at/
JH
JH – Jakobshaven Glacier Offset tracking
Surface Motion Product Based on InSAR and Offset Tracking

## Slide 37
References
Bamler, R. and Hartl, P.: Synthetic aperture radar interferometry, Inverse Problems, 14, R1 - R54, 1988.
Doyle, H.S., Hubbard, A., van de Wal, R.S.W. et al. Amplified melt and flow of the Greenland ice sheet driven by late-summer cyclonic rainfall. Nature Geosc., 8, doi: 10.1038/NGEO242, 2015.
ESA SP-1322/1: Sentinel-1: ESA’s Radar Observatory Mission for GMES Operational Services. March 2012.
Hanssen, R.F.: Radar Interferometry, Data Interpretation and Error Analysis. Kluwer Academic Publishers, 2001.
Krieger, G., Zink, M., Bachmann, M., Bräutigam, B., Schulze, D., Martone, M., Rizzoli, P., Steinbrecher, U., Anthony, J. W., et al.: TanDEM-X: a radar interferometer with two formation flying satellites, Acta Astronaut., 89, 83–98, doi:10.1016/j.actaastro.2013.03.008, 2013.
Magnússon, E., Rott, H., Björnsson, H., Pálsson, F.: The impact of jökulhlaups on basal sliding observed by SAR interferometry on Vatnajökull. J. Glaciol., 53 (181), 232-240, 2007.
Mätzler, C. Applications of the interaction of microwaves with the natural snow cover. Remote Sensing Review, 2, 259-387, 1987.
Moreira, A., Prats-Iraola, P., Younis, M., Krieger, G., Hajnsek, I., Papathanassiou, K.: A tutorial on synthetic aperture radar, IEEE Geosci. Rem. Sens. Mag., 1(1), 6–43, https://doi.org/10.1109/MGRS.2013.2248301, 2013.
Oliver, C., Quegan, S.: Understanding Synthetic Aperture Radar Images. Artech House, Boston, London, 1998.
Rott, H., Sturm, K.,. Miller, H.: Active and passive microwave signatures of Antarctic firn by means of field measurements and satellite data. Ann. Glaciol., 17, 337-343, 1993.
Rott, H., Abdel Jaber, W., Wuite, J. et al.: Changing pattern of ice flow and mass balance for glaciers discharging into the Larsen A and B embayments, Ant. Peninsula, 2011 to 2016. The Cryosphere, 12, 1273-1291, 2018..
Rott, H., Scheiblauer, S., Wuite, J., Krieger, L., Floricioiu, D., Rizzoli, P., Libert, L., Nagler, T.: Penetration of interferometric radar signals in Antarctic snow. The Cryosphere, 15, 4399–4419, 2021.
Ulaby, F.T. and Long, D.G.: Microwave and Radar Remote Sensing, Univ. Michigan Press, Ann Arbor, 2014.
X. Xu, D. Liang, L. Tsang, K. M. Andreadis, E. G. Josberger et al.: Active remote sensing of snow using NMM3D/DMRT and comparison with CLPX II airborne data. IEEE J. Sel. Topics Appl. Earth Observ. Remote Sens., vol. 3, 689–697, 2010.